## Slide 1: Updates on 3D OpenROAD Database
Osama Hammad
Cho Moon
Precision Innovations is the primary industrial developer of OpenROAD and provides commercial support and customization for OpenROAD.
precision

## Slide 2: P&R for 3D IC Designs
OpenROAD database (ODB) has been enhanced to read, write, visualize, analyze and optimize 3D designs
  We want to invite more adoption of open-source tools and improve collaboration
3Dblox format is used for design I/O
One design = multiple dies, multiple processes, bonded together
  Each die/chiplet can have its own PDK and TechLEF
ODB now models this end to end with persistency (write_db & read_db without data loss)
  “Unfolded view” is available to enable full chip analysis for linting, visualization, timing analysis
No more layer stack “hacks” for 3D designs

## Slide 3: 3D Viewer and Linter
Check | Purpose
Logical connectivity | Physically aligned bump pairs that belong to different nets.
Floating chips | Flags chip sets that aren't reachable to "ground". They're floating in the design
Overlapping chips | die chiplets whose 3D bounding boxes overlap.
Internal-ext usage | INTERNAL_EXT regions not referenced by any connection.
Connection regions | Connections whose regions don't xy-overlap or whose mating-surface gap mismatches the connection thickness.
Bump physical alignment | Bumps sitting outside their parent region's footprint.
Alignment markers | Missing, duplicate, or mis-oriented alignment markers between connected chips.

## Slide 4: 3D STA and RC Extractor

## Slide 5: Yield Analysis
YAP from UCLA has been integrated into OpenROAD via a file-based interface
  Bond failure can be analysed
  Heat map can be displayed

## Slide 6: 3D Database Overview
dbChip
Type: DIE | HIER | RDL | IP | SUBSTRATE
dbBlock
dbTech
TechLEF per chip
dbChipRegion
front | back | internal | internal_ext
dbChipBump
bumpmap
dbChipInst
placed at (x, y, z) with dbOrientType3D
dbChipRegionInst
one per parent dbChipInst
dbChipBumpInst
Located on dbChipRegionInst
instantiates
instantiates
dbChipNet
logical net spanning bump insts
instantiates
connects
dbChipConn
region <-> region with thickness
connects
Same pattern as dbMaster / dbInst, lifted one level up to the chip itself.

## Slide 7
3DBlox Files (3dbx and 3dbv)
ChipletDef:
compute_tile:
type: die
design_area: [1000, 1000]
thickness: 50
regions:
to_interposer: side: back coords: [[...]...]
bmap: compute_tile.bmap
external: APR_tech_file: [tech_5nm.lef]
cache_die: .........
dbChip
dbChipRegion
dbTech
dbChipBump
read_3dbv chiplet_definitions.3dbv
Design: name: top_design external:
verilog_file: “top.v” ChipletInst: cpu_inst: reference: cpu_complex ... Stack: interposer_inst: loc: [0,0] z: 0.0 orient: R0 ... Connection: Conn1: top: interposer_inst.regions.to_cpu
bot: cpu_inst/compute_inst.regions.to_interposer
thickness: 10.0
dbChipInst
dbChipConn
read_3dbx top_design.3dbx
dbChip(HIER)
Notes: 3dbx contains chiplet connections
3dbv contains chiplet details

## Slide 8: Additional Documentation
https://github.com/The-OpenROAD-Project/OpenROAD/blob/master/src/odb/doc/3dic.md